## Slide 1
SUNFLOWER
Solar Panel Controller
An Intelligent, Autonomous Solar Tracking & Monitoring System
Competition Presentation | April 2026
ESP32 • L298N Motor • Servo • RTC • WiFi TCP • OLED

## Slide 2
THE PROBLEM
Why fixed solar panels are not enough
25 – 40%
Energy Lost
Fixed panels miss peak sun because they cannot track the sun's movement across the sky. A panel pointed east loses hours of afternoon output.
Manual Only
No Automation
Repositioning panels by hand is impractical, especially on rooftops, remote farms, or large-scale solar fields with hundreds of panels.
Zero Visibility
No Monitoring
Most DIY systems have no way to know current power output, battery health, or whether the system is working — until something fails.
Weather Damage
No Protection
Panels left fully exposed during storms, hail, or high wind events are at risk of physical damage. Automated retraction prevents this.
High Cost
Barrier to Entry
Commercial solar trackers cost thousands of dollars, making them inaccessible for small farms, rural homes, and developing regions.
No Remote View
Operator Blind
Installers and owners have no remote dashboard to see live voltage, current, and power — making fault diagnosis slow and expensive.
Our system solves all six problems with a single $30 device.

## Slide 3
WHAT THE SYSTEM DOES
Inspired by the sunflower — follows the sun from dawn to dusk
OPEN
Opens panel at sunrise
RTC-scheduled DC motor fires at programmed morning time, physically deploying the solar panel to face the sky.
TRACK
Tracks sun every 15 minutes
Continuous-rotation servo rotates the panel angle toward the sun at 15-minute intervals throughout the day.
CLOSE
Closes panel at sunset
Motor reverses at programmed evening time, retracting the panel to protect it from wind, rain, and vandalism overnight.
MONITOR
Monitors output live
ACS712 current sensor + voltage dividers measure panel voltage (V), current (A), and calculated power (W) every 100 ms.
DISPLAY
Wireless OLED dashboard
A separate ESP32 shows live sensor values on an OLED screen over a private WiFi network — no internet required.
OVERRIDE
Manual control anytime
4 physical buttons let the operator manually open/close the panel or nudge the servo angle at any time.
RESET
Emergency stop
A single RESET command instantly halts motor and servo, clears all state flags — safe for field use.
CALIBRATE
Auto sensor calibration
On every boot, 500 ADC samples are averaged to auto-calibrate the zero-current offset — no manual tuning needed.

## Slide 4
SYSTEM ARCHITECTURE
Two ESP32 units — fully wireless, no internet required
Solar Controller (ESP32 — Client)
▶ L298N DC Motor Driver
▶ Continuous Rotation Servo
▶ Panel Voltage Sensor (GPIO 34)
▶ Panel Current Sensor ACS712 (GPIO 35)
▶ Battery Voltage Sensor (GPIO 32)
▶ RTC DS3231 — I²C timekeeping
▶ WiFi Station mode — TCP client
▶ Non-blocking 10ms loop
▶ PWM soft-ramp motor control
▶ Auto current sensor calibration
►
◄
WiFi TCP
Sensor CSV (100ms)
Button Commands
Remote Control Unit (ESP32 — AP)
▶ WiFi Access Point (192.168.4.1:5000)
▶ OLED 128×64 live dashboard
▶ Displays: Panel V, Current A, Power W
▶ Displays: Battery V, Time (HH:MM:SS)
▶ Button 1 — SERVO_FWD (hold to run)
▶ Button 2 — SERVO_REV (hold to run)
▶ Button 3 — PANEL_OPEN (hold to run)
▶ Button 4 — PANEL_CLOSE (hold to run)
▶ Auto-reconnects dropped clients
▶ Display refresh every 500ms

## Slide 5
KEY TECHNICAL FEATURES
Engineering decisions that make the system reliable in the field
Non-Blocking Architecture
• Main loop runs every 10 ms — never uses delay()
• All operations use millis() timers (motor, servo, WiFi, sensors)
• Motor, servo and WiFi reconnect all run concurrently without pausing each other
• WiFi connect() is only called when motor is IDLE to prevent blocking the PWM ramp
Motor State Machine
• States: MOTOR_IDLE → OPENING / CLOSING / MANUAL → IDLE
• New commands only accepted when state is MOTOR_IDLE — prevents double-trigger
• opened/closed flags set AFTER motor physically finishes — reflects real world
• Emergency RESET command instantly halts motor, servo, and clears all flags
PWM Soft-Ramp Control
• Custom MotorL298N library ramps 0→90% over ~5 seconds
• 30% kickstart PWM prevents stall against static friction on startup
• hardBrake() instantly cuts all PWM — used during RESET
• Smooth ramp reduces mechanical shock, extends belt and gear life significantly
Automatic Sensor Calibration
• ACS712 zero-current offset auto-calibrated on every boot
• Averages 500 ADC samples over 1 second before accepting load
• Eliminates offset drift from temperature and supply voltage variation
• No manual potentiometer tuning required — works out of the box
Servo Sun Tracking
• Auto-tracking fires every 15 minutes while panel is open
• Duration calculated from RPM and revolutions (not guessed)
• Manual override has highest priority — auto-track pauses instantly
• Tracking cancelled automatically when panel closes at end of day
Data Transmission
• CSV sent over TCP every 100 ms: time, V, A, W, battery V
• RTC cached every 1 second — avoids I²C overhead every 10 ms loop
• WiFi auto-reconnects every 5 seconds if connection drops
• Button press edge-detected with 200 ms debounce; release is immediate

## Slide 6
COMMUNICATION PROTOCOL
Private WiFi — TCP — no cloud, no internet, no latency
Controller → Remote (every 100 ms)
Format: HH:MM:SS , voltage , current , power , batteryVoltage
Example: 08:42:15 , 18.34 , 2.10 , 38.51 , 12.67
Field
Unit
Source
HH:MM:SS
Time
DS3231 RTC
voltage
V
Panel voltage divider GPIO 34
current
A
ACS712 current sensor GPIO 35
power
W
Calculated: voltage × current
batteryVoltage
V
Battery voltage divider GPIO 32
Remote → Controller (on button press/release)
Command
Trigger
Effect
SERVO_FWD
Hold button 1
Servo rotates forward — manual sun tracking
SERVO_REV
Hold button 2
Servo rotates reverse — undo tracking angle
SERVO_STOP
Release button 1 or 2
Servo stops immediately on release
PANEL_OPEN
Hold button 3
DC motor opens panel (only if MOTOR_IDLE)
PANEL_CLOSE
Hold button 4
DC motor closes panel (only if MOTOR_IDLE)
MOTOR_STOP
Release button 3 or 4
Motor stops immediately on release
RESET
Emergency
Halts everything, clears all state flags

## Slide 7
LARGE SCALE IMPLEMENTATION
How this prototype scales to a commercial solar farm
Hardware Scaling
• Replace ESP32 with Raspberry Pi / industrial PLC as central hub
• L298N → 3-phase motor controllers for larger actuators
• Single servo → stepper motors with encoders for precise angular control
• Voltage dividers → industrial CT clamps rated for high currents (100A+)
• OLED → web-based Grafana/React dashboard for fleet-wide metrics
• Add dual-axis trackers: separate motor for elevation angle control
Network & Software Scaling
• Replace direct TCP with MQTT broker (Mosquitto) — each panel is a topic
• OTA (Over-the-Air) firmware updates across entire field without physical access
• Time-series database (InfluxDB / TimescaleDB) for historical analysis
• REST API so any device (phone, browser, SCADA) can query panel status
• GPS-based sun angle calculation from latitude/longitude using NOAA formulas
• Cloud backup with daily energy yield reports sent via email/SMS
Physical Deployment
• Single-axis tracker (east-west) driven by DC motor — most common commercial design
• Dual-axis tracker adds elevation control for maximum annual yield
• Wind speed sensor auto-retracts all panels when gusts exceed safe threshold
• IP65 weatherproof enclosures for all electronics; surge protection on sensors
• Modular wiring harness — each panel unit is identical, plug-and-play
• Remote diagnostic port: plug in laptop to pull logs without disassembly
Operations at Scale
• Central dashboard shows all panels on a map — green/amber/red status
• Predictive maintenance: compare daily yield to expected yield, flag underperformers
• Automated fault detection: if panel V drops unexpectedly, send SMS alert
• Staggered motor schedules to avoid current surge when 100 panels open at once
• Role-based access: operators can view, admins can reconfigure schedules
• Audit log of all commands and state changes for insurance and warranty claims

## Slide 8
SYSTEM IMPROVEMENTS
Upgrades to transform the prototype into a production-grade system
Precision Sun Tracking
• Add LDR (light-dependent resistor) pair — servo stops when both read equal light
• Closed-loop: encoder on servo shaft confirms actual angular position
• MPPT algorithm — track angle that maximises real-time power, not just sun direction
• Add elevation axis motor for full 2-axis tracking (+15% extra yield over single axis)
• Store tracking history to learn seasonal patterns and anticipate sun position
Reliability & Safety
• Motor stall detection — dedicated current sensor on motor supply line
• Panel position encoder — know exact open angle, prevent over-driving
• ESP32 hardware watchdog — auto-reboot if firmware hangs
• Redundant NTP time sync when WiFi is available; RTC as offline fallback
• Surge protection and reverse-polarity protection on all power inputs
Energy Intelligence
• State-of-charge calculation from battery voltage discharge curve
• Watt-hour accumulation — log daily energy yield (kWh) to flash memory
• Low battery alert — automatically retract panel and go to sleep mode
• Compare actual vs expected yield — alert if efficiency drops below threshold
• Temperature sensor on panel — derate power estimate on hot days (3% per °C)
User Interface
• Replace OLED with colour TFT touchscreen showing voltage/current/power graphs
• Mobile app via Bluetooth for configuration (set open/close times, tracking interval)
• Push notifications when power drops below expected or a fault is detected
• Voice alerts via small buzzer — different tones for open, close, fault events
• Web interface with historical charts, exportable CSV, and remote schedule config
Connectivity
• MQTT over WiFi to a local home server or cloud broker (AWS IoT / HiveMQ)
• LoRa radio fallback for installations beyond WiFi range (up to 10km line-of-sight)
• 4G LTE module option for completely off-grid sites with no WiFi infrastructure
• Mesh networking — controllers relay data through each other to the gateway
• Encrypted TLS communication to prevent command injection over the air
Manufacturing & Deployment
• Custom PCB to replace breadboard wiring — reduces failure points significantly
• Conformal coating on PCB for humidity and corrosion resistance
• 3D-printed weatherproof enclosure with cable glands and DIN rail mount
• Factory calibration routine — automated test jig checks each unit before shipping
• QR code on each unit links to its data dashboard and service history

## Slide 9
FUTURE BENEFITS & APPLICATIONS
Why this technology matters beyond the competition
Energy Independence
• Single-axis tracker increases annual yield by 25–40% over fixed panels
• Dual-axis tracking adds a further 10–15% on top of single-axis
• Fewer panels needed for the same power target — lower land and material cost
• Longer battery cycle life: tracker extracts full energy during peak sun hours
• Enables off-grid homes, farms, and villages to become energy self-sufficient
Agricultural (Agrivoltaics)
• Tilted panels let morning/evening light through while blocking harsh midday sun
• Crops grown underneath benefit from shade — up to 60% less water consumption
• Dual income: farmers sell electricity AND grow crops on the same land
• This system’s tilt angle control makes it a ready foundation for agrivoltaics
• Already deployed at scale in Japan, Germany, and South Korea
Smart Grid Integration
• Real-time power data at 100ms resolution feeds directly into grid balancing
• When panels report excess generation, smart switches divert energy to EV charging
• Demand-response: utilities can remotely schedule open/close times to shift load
• Micro-grid: cluster of these units can power a village with automatic load sharing
• Predictive generation forecast helps grid operators plan backup generation
Developing World & Disaster Relief
• No internet required — the two ESP32s form their own private WiFi network
• Total BOM cost under ₹2500 (∼$30) — accessible to smallholder farmers globally
• Can be assembled with basic tools and locally available components
• Solar tracker + battery means uninterrupted power even in remote locations
• Deployed to disaster zones as portable power stations for medical equipment
Environmental Impact
• Every 1% yield improvement = proportionally fewer panels for a given power target
• Fewer panels = less silicon, aluminium, and rare earth mining required
• 1 MW solar farm with tracking: +350 kWh/day = saves ~50,000 kg CO₂/year
• Retractable panels survive hailstorms — longer panel life, less e-waste
• Closed-loop MPPT maximises green energy extraction without any fuel burning
Commercial & Research Opportunities
• Platform for AI-based sun prediction using historical tracking data
• University research tool for studying panel degradation and soiling effects
• Integration with weather APIs to pre-position panels before storms arrive
• Data marketplace: anonymised energy yield data valuable to grid planners
• White-label product for solar installation companies to brand and resell

## Slide 10
REAL-WORLD IMPACT
Quantified energy gains from single-axis solar tracking
+35%
Average annual energy gain from single-axis tracking vs fixed panel
+50%
Peak-hour energy gain on clear summer days
100ms
Sensor data refresh rate — real-time monitoring for every panel
₹2500
Total Bill of Materials cost for the complete two-unit system
15 min
Sun tracking interval — optimal balance of yield vs servo wear
50,000 kg
CO₂ saved per year for a 1 MW farm using this tracker
Based on 35% improvement from single-axis tracking, 300 sunny days/year, 0.4 kg CO₂/kWh grid average (IEA 2024)

## Slide 11
COMPETITIVE ADVANTAGES
What makes this system stand out
01
No Internet Required
The two ESP32s form a private WiFi network. Works in fields, deserts, rooftops — anywhere with no infrastructure. Unlike cloud-dependent systems, it cannot be killed by a server outage.
02
Custom PWM Motor Library
Soft-ramp 0→90% over 5 seconds with kickstart — prevents gear shock, motor burnout, and belt snap. No commercial tracker at this price point offers configurable ramp control.
03
Self-Calibrating Sensors
ACS712 zero offset auto-calibrated on every boot with 500 samples. Eliminates manual potentiometer tuning and compensates for temperature drift automatically over the lifetime of the unit.
04
State-Machine Safety
Motor only accepts a new command when IDLE — impossible to trigger opening while already opening. Flags are set after physical completion, not on command issue, reflecting real-world state.
05
100ms Live Data Stream
10 readings per second over TCP gives a smooth, real-time view of voltage, current, and power. Enough resolution to detect transient shadows, partial shading, and wiring faults.
06
Extensible Command Protocol
Adding a new button or remote command requires one line in the buttons[] array — no other code changes. Engineers can add features in minutes without understanding the full codebase.
07
Emergency Reset
A single RESET command stops motor, stops servo, clears all flags and timers instantly. Designed for field safety — operator presses one button and the entire system is in a known safe state.
08
Under ₹2500 Total Cost
Complete two-unit system costs under ₹2500 using off-the-shelf modules. Commercial solar trackers start at ₹40,000+. This makes professional-grade tracking accessible to small farmers globally.

## Slide 12
BILL OF MATERIALS
Complete hardware cost — under ₹2500 for the full system
Component
Qty
Unit Price
Total
Purpose
ESP32 Dev Board
2
₹400
₹800
Main controller + Remote control unit
L298N Motor Driver Module
1
₹150
₹150
DC motor direction and PWM speed control
DC Gear Motor (12V)
1
₹350
₹350
Opens and closes the solar panel
Continuous Rotation Servo
1
₹280
₹280
Sun tracking axis rotation
ACS712-30A Current Sensor
1
₹120
₹120
Panel output current measurement
Voltage Divider Module
2
₹45
₹90
Panel voltage + battery voltage sensing
DS3231 RTC Module
1
₹180
₹180
Real-time clock for open/close scheduling
SSD1306 OLED 128×64
1
₹220
₹220
Live sensor dashboard on remote unit
Push Buttons (pack)
1
₹50
₹50
4 control buttons on remote unit
Miscellaneous (wires etc)
1
₹200
₹200
Jumper wires, breadboard, capacitors, resistors
TOTAL
₹2,440

## Slide 13
CONCLUSION
1. Low-cost hardware, professional results
Under ₹2500 of components delivers intelligent, autonomous solar tracking — capabilities previously only available in ₹40,000+ commercial systems.
2. Non-blocking, state-machine firmware
Motor, servo, WiFi, and sensors all run concurrently on a single microcontroller. The software architecture is sound enough to scale to production.
3. Wireless and self-contained
No internet, no cloud, no single point of failure. The two-unit system forms its own private network — deployable anywhere on Earth.
4. Clear upgrade path
LDR closed-loop tracking, MPPT, MQTT, OTA updates, custom PCB — every improvement is well-defined and builds directly on the existing architecture.
5. Measurable real-world impact
+35% annual energy yield, 50,000 kg CO₂ saved per MW, and a ₹2500 price point that makes solar tracking accessible to smallholder farmers worldwide.
"The future of solar is not just bigger panels — it is smarter panels that follow the sun, report their health, and respond to their environment automatically."